## Slide 1: File format(s) to save from behaviors with Bonsai? 08/30/2021

## Slide 2
It is critical that Bonsai data outputs can interface with our existing analysis pipelines.
There are a lot of drawbacks to our current system (saving all behavior data + metadata in a pickle file), and switching to Bonsai presents an opportunity to rethink our approach.
Starting statements

## Slide 3
In Bonsai, it is incredibly easy to do two things:
  Trigger a digital output on a software event and sending that event to a dedicated sync line.
  Write timestamped data to a CSV file
Proposal:
  Any events relevant to the task or stimulus are associated with both a digital on/off transition recorded by the sync computer
  Additional metadata stored in a CSV file.
  At the end of the experiment, package all of this into a single file (pickle or otherwise), assuming a minimal amount of bookkeeping to keep track of which sync lines are associated with which type of events.

## Slide 4
PROS | CONS | MITIGATION
More "lightweight" and language-agnostic than what is used by Camstim | Work to define consistent conventions that can be used across experiment | 
Our pipeline sync hardware and wiring boxes have 6 available sync lines with another 10 (for a total of 16) that could be made available with changes to the sync box | No sync boxes on behavior clusters | Alternative saving strategy for behavioral boxes?
This concept was tested during the piloting efforts | Need to be defined + development efforts. | 
The sync system is fundamentally our reference temporal system and has the highest temporal precision and reliability. |  | 
Sync files are efficient and lightweight: They only store state transitions in an hdf5 file, thereby minimizing data storage required. |  | 
We already are experienced handling and using h5 sync files throughout the whole data collection and analysis pipeline. | Existing codebases accessing pkl files for behavioral and physiology analyses | Continue support our legacy Camstim and pkl system
NWB files stores stimulus information in a stimulus trial table which uses the same storage scheme: Individual events have a name, a start and end timestamps associated to it |  | 
This simple storage scheme provides a great deal of flexibility on how behavioral events are recorded. Each scientific team can leverage available sync lines within Bonsai in a way that fits their scientific requirements. |  | 
Data transfer from the experimental rigs to internal file storage registered by LIMS. Those systems are maintained by MPE and can already handle various data formats produced by the instruments | Break backward compatibility | Backward compatibility was already somehow broken with pkl files
 | Data conversion from pkl files to LIMS database and the associated interaction with mTRAIN. | A strategy to do that needs to be agreed upon. Will happen in phase 2.
 | Mouse-seeks access to behavior pkl files information. Mouse-seeks provide immediate analysis to behavioral data from pkl files to monitor basic metrics. | Will happen in phase 2?

## Slide 5
Path forward?
Implement a beta set of output files for detection of change
Formalize file format in a standardized document
Circulate among stakeholders (MPE, TECH, NWB, SCIENTISTS)
Get Approval or iterate.
Implement a second behavior (?) with it